General formatting:

0x 00 03 02 08 02 0B 06

first byte is destination/reciever (0 = controller, 2 = pump, 15 = oven, AS = 13)
Second byte is the length of the message, does not include first 3 bytes
third byte is the sender
Might be able to do testing with arduino on live system by giving it a unique address

if 4th byte = 0x02 then that is a read, if it is 0x03 is is a write

Last byte is all previous bytes XORed together
 the ACK byte is 0x06

Init on power-up
00 04 0D 00 01 0D 05 06
0D 04 00 00 01 0D 05 06
02 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF E2 06
02 05 00 30 0D FF 0F CA 06
0D 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF ED 06
0D 05 00 30 0D FF 0F C5 06
0F 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF EF 06
0F 05 00 30 0D FF 0F C7 06
0D 09 00 00 03 00 01 00 00 00 00 06 06
00 09 0D 00 03 00 01 00 00 00 05 03 06
00 03 0D 08 01 07 06
hardware pins

ethernet

1 orange white gnd
2 orange
3 green white pump enable?
4 blue controller command to inject?
5 blue white seems to be unused
6 green VCC
7 brown white COMMs
8 brown gnd

J9 on controller
1 gnd
2
3
4
5
6
7
8
9 vcc
10 gnd
Pump
Note: STA2 includes STAT, but STA2 inludes a lot more stuff
Get status STA2 2 responded with hex 5354 4132 2020 3200 2002 0100 0302 0101 (0384 flow a) (0064flow b) 0000 0000 0000 0000 pump off, 90%,10%,0%,0%, flow set to 0.100 max pressure = 200, min = 0
02 03 00 02 1C 1F 06
00 0B 02 02 1C 00 01 01 00 03 02 01 01 16 06	auto (original data)
00 0B 02 02 1C 00 01 01 01 04 02 01 01 10 06	manual in menu
00 0B 02 02 1C 00 00 01 01 04 02 01 01 11 06	manual out of menu
00 0B 02 02 1C 00 01 01 00 04 02 01 01 11 06	manual pump off
00 0B 02 02 1C 00 01 01 00 01 02 01 01 14 06	manual high pressure fault
02 03 00 02 14 17 06
00 0F 02 12 14 00 00 03 84 00 00 32 00 00 00 00 00 BE 06 90%a 5%b 0%c 5%d
00 03 02 30 32 03 06
02 03 00 02 15 16 06
00 07 02 02 15 00 00 00 00 12 06 current flow rate
02 03 00 02 16 15 06
00 07 02 02 16 00 00 00 00 11 06 current pressure in BAR

STAT 2 responded with STAT 2# 1 1 1 3 2 1 1
02 03 00 02 1C 1F 06
00 0B 02 02 1C 00 01 01 00 03 02 01 01 16 06
00 04 02 0A 11 00 1D 06 00 03 02 08 02 0B 06
STAT 2# 2 1 0 3 2 1 1
00 0B 02 02 1C 00 01 01 00 03 02 01 01 16 06
STAT 2# 2 1 0 4 2 1 1
00 0B 02 02 1C 00 01 01 00 04 02 01 01 11 06 pump off manual
STAT 2# 1 1 1 4 2 1 1
00 0B 02 02 1C 00 00 01 01 04 02 01 01 11 06 pump on manual
STAT 2# 1 1 1 3 2 1 1
00 0B 02 02 1C 00 00 01 01 03 02 01 01 16 06 pump on auto
STAT 2# 2 1 0 1 2 1 1
00 0B 02 02 1C 00 01 01 00 01 02 01 01 14 06	pump high pressure fault manual
STAT 2# 2 1 0 4 2 1 1
00 0B 02 02 1C 00 01 01 00 04 02 01 01 11 06	pump fault cleared
STAT 2# 2 1 0 1 2 1 1
00 0B 02 02 1C 00 01 01 00 01 02 01 01 14 06	pump low pressure fault
STAT 2# 2 1 1 2 2 1 1
00 0B 02 02 1C 00 01 01 01 02 02 01 01 16 06	pump running a method
STAT 2# 1 1 1 3 2 1 1
00 0B 02 02 1C 00 00 01 01 03 02 01 01 16 06
STAT 2# 2 1 1 2 2 1 1
00 0B 02 02 1C 00 01 01 01 02 02 01 01 16 06
STAT 2# 1 1 1 3 2 1 1
00 0B 02 02 1C 00 00 01 01 03 02 01 01 16 06
pump turned on, volunteered
00 03 02 08 01 08 06
00 04 02 08 13 01 1C 06
pump turned off, volunteered
00 03 02 08 02 0B 06
00 04 02 08 13 00 1D 06
pump fault low pressure, volunteered
00 03 02 08 02 0B 06
00 05 02 0E 02 04 01 0E 06
pump fault high pressure, volunteered
00 05 02 0E 02 04 01 0E 06
00 03 02 08 02 0B 06

pump on PUMP 2 1	turn pump on or off
02 04 00 0A 11 00 1D 06
00 04 02 0A 11 00 1D 06
00 03 02 08 01 08 06	//volounteers this when pump changes state

MUST 2 //pump init?
02 04 00 0A 16 01 1B 06
00 04 02 0A 16 00 1A 06

GPIB programming (PRG2 2)
5052 4732 2020 32[20 2031 2020 32 seems to be constant][20 2032 3034max pressure] [2020 2020 30 min pressure][20 2020 2034 number of lines in program] 20[00 0000 00time 1 in seconds][03 84 %a][00 64%b][00 00%c][00 00%d?][00 64 flow rate 1]FF FFFF FF[00 0000 42 time 2][03 20%a2][00 C8 %b2][00 00%c2][00 00%d2][FF FF flow rate 2]FF FFFF FF[00 0000 84 time3][02 BC%a3][01 2C %b3][00 00%c3][00 00%d3][00 C8flow rate 3]FF FFFF FF[00 0000 B4 time 4][02 58%a4][01 90%b4][00 00%c4][00 00%d4][01 2C flow 4]FF FFFF FF

CLEA 2 clears fault remotely!
02 03 00 01 05 05 06
STOP 2
02 03 00 01 03 03 06
STAR 2
02 03 00 01 01 01 06

PEND 2
02 03 00 06 04 03 06
00 04 02 06 04 83 87 06

PRER 2	responds the same if the pump is faulted/running or not
02 03 00 07 10 16 06
00 07 02 07 10 00 00 00 00 12 06

INIT 2
02 04 00 0A 16 02 18 06
00 04 02 0A 16 00 1A 06

COND 2	//same as STA2, but returns in ASCII instead of HEX
02 03 00 02 14 17 06
00 0F 02 12 14 00 00 03 84 00 00 32 00 00 00 00 00 BE 06
00 03 02 30 32 03 06
02 03 00 02 15 16 06
00 07 02 02 15 00 00 00 64 76 06 02 03 00 02 16 15 06
00 07 02 02 16 00 00 00 00 11 06

OPTI 2
02 03 00 0A 14 1F 06
00 04 02 0A 14 84 9C 06

MANU 2	seems to have turned off pump, first line might be manually setting proportioning valves
02 0F 00 13 14 00 00 01 00 00 50 00 00 64 00 00 32 0D 06
02 0B 00 30 00 00 3C 00 00 00 00 00 00 05 06 00 04 02 03 14 00 11 06

PTST 2 0 20	autosends pressure every 2 seconds on/off
02 07 00 03 01 00 00 00 14 13 06
00 04 02 03 01 00 04 06

PRSG 2 current pressure maybe?
02 03 00 02 16 15 06
00 07 02 02 16 00 00 00 00 11 06

MNTE 2 1? MNTE also goes with AS
02 04 00 07 13 01 13 06
00 0C 02 07 13 00 01 01 00 01 5F 01 1D 03 5B 06

IDNP 2
02 03 00 02 1D 1E 06
00 0F 02 12 1D 00 00 00 00 00 00 00 00 00 00 00 00 02 06
00 07 02 30 00 00 00 00 00 35 06
02 03 00 02 1E 1D 06
00 0F 02 12 1E 00 00 00 00 00 00 00 00 00 00 00 00 01 06
00 07 02 30 00 00 00 00 00 35 06

PRG2 2
5052 4732 2020 32[20 2031 2020 32 seems to be constant][20 2032 3034max pressure] [2020 2020 30 min pressure][20 2020 2034 number of lines in program] 20[00 0000 00time 1 in seconds][03 84 %a][00 64%b][00 00%c][00 00%d?][00 64 flow rate 1]FF FFFF FF[00 0000 42 time 2][03 20%a2][00 C8 %b2][00 00%c2][00 00%d2][FF FF flow rate 2]FF FFFF FF[00 0000 84 time3][02 BC%a3][01 2C %b3][00 00%c3][00 00%d3][00 C8flow rate 3]FF FFFF FF[00 0000 B4 time 4][02 58%a4][01 90%b4][00 00%c4][00 00%d4][01 2C flow 4]FF FFFF FF

5052 4732 2020 3220 2031 2020 32	address
20 2032 3430 max pressure 240
2020 2032 35	min pressure 25
20 2020 2037	number of lines 7
20	constant
0000 0000	time 1 0
03 8400 3200 3200 00	%abcd 1 900/50/50/0
00 64	flow 1 100
FF FFFF FF	end
000000 35	time 2 53
03 2000 3200 9600 00	%abcd 2 800/50/150
FF FF	flow 2 unchanged
FF FFFF FF	end
000000 42	time 3 66
02 BC00 3200 FA 00 00	%abcd 3 700/50/250
00 64	flow 3 100
FF FFFF FF
000000 48	time 4 72
02 5800 3201 5E00 00	%abcd 4 600/50/350
00 32	flow 4 50
FF FFFF FF
000000 4D	time 5
02 6200 3201 5400 00	%abcd 5
FF FF	flow 5
FF FFFF FF
000000 53	time 6
02 6C00 3201 4A00 00	%abcd 6
00 28	flow 6
FF FFFF FF
000000 5A	time 7
00 0001 F401 F400 00	%abcd 7
00 28	flow 7
FF FFFF FF

02 04 00 0A 16 01 1B 06
00 04 02 0A 16 00 1A 06
02 05 00 06 01 01 02 03 06
00 04 02 06 01 00 01 06
02 09 00 06 02 00 00 F0 00 00 19 E6 06	//max pressure 240 min pressure 25
00 04 02 06 02 00 02 06

02 0F 00 16 03 00 00 00 00 00 03 84 00 00 32 00 00 AD 06 time 0 %a 900 %2 50 %3 50 %4 0
02 0D 00 30 32 00 00 00 00 00 64 FF FF FF FF 69 06	flow 1 100

00 04 02 06 03 00 03 06
02 0F 00 16 03 00 00 00 35 00 03 20 00 00 32 00 00 3C 06	time 2 52 sec %a 800
02 0D 00 30 96 00 00 00 FF FF FF FF FF FF FF 56 06	flow unchanged

00 04 02 06 03 00 03 06
02 0F 00 16 03 00 00 00 42 00 02 BC 00 00 32 00 00 D6 06	time 3 66 sec %a 700
02 0D 00 30 FA 00 00 00 00 00 64 FF FF FF FF A1 06

00 04 02 06 03 00 03 06
02 0F 00 16 03 00 00 00 48 00 02 58 00 00 32 00 01 39 06
02 0D 00 30 5E 00 00 00 00 00 32 FF FF FF FF 53 06
00 04 02 06 03 00 03 06
02 0F 00 16 03 00 00 00 4D 00 02 62 00 00 32 00 01 06 06
02 0D 00 30 54 00 00 00 FF FF FF FF FF FF FF 94 06
00 04 02 06 03 00 03 06
02 0F 00 16 03 00 00 00 53 00 02 6C 00 00 32 00 01 16 06
02 0D 00 30 4A 00 00 00 00 00 28 FF FF FF FF 5D 06
00 04 02 06 03 00 03 06
02 0F 00 16 03 00 00 00 5A 00 00 00 00 01 F4 00 01 B6 06
02 0D 00 30 F4 00 00 00 00 00 28 FF FF FF FF E3 06
00 04 02 06 03 00 03 06
02 03 00 06 04 03 06
00 04 02 06 04 00 04 06
02 04 00 0A 16 02 18 06
00 04 02 0A 16 00 1A 06

Pump init on power-on
00 04 02 00 01 02 05 06
02 04 00 00 01 02 05 06
02 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF E2 06
02 05 00 30 0D FF 0F CA 06
0D 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF ED 06
0D 05 00 30 0D FF 0F C5 06
0F 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF EF 06
0F 05 00 30 0D FF 0F C7 06
02 09 00 00 03 00 01 00 00 00 00 09 06
00 09 02 00 03 00 00 00 00 00 06 0E 06
00 03 02 08 02 0B 06

Pump fizzing
0203 0002 0201
0005 0202 0100 0105

0203 0002 0300
000F 0212 0200 2020 2020 2038 3130 3738 313A
0006 0230 302D 3030 29

0203 0002 0407
0005 0202 0300 0107

0203 0002 0506
error, don’t do it

0203 0002 1417
000F 0212 1400 0003 8400 0032 0000 0000 00BE
0003 0230 3203

0203 0002 1615
0007 0202 1500 0000 0012

0203 0002 1714
0007 0202 1600 0000 0011

0203 0002 181B
0008 0202 1700 0000 0000 1F

0203 0002 1A19
0005 0202 1900 001C

0203 0002 1B18
0005 0202 1A00 011E

0203 0002 1C1F
0005 0202 1B00 011F

0203 0002 1D1E
000B 0202 1C00 0101 0003 0201 0116

0203 0002 1E1D
000F 0212 1D00 0000 0000 0000 0000 0000 0002
0007 0230 0000 0000 0035

0203 0002 1F1C
000F 0212 1E00 0000 0000 0000 0000 0000 0001
0007 0230 0000 0000 0035

Oven

Oven power-on <rtansmitted> 0x00040f 00010f05<ack> <0f040000010f05> ACK <0f0f001002ff02ffffffffffffffffffffef> ACK <0f0500300dff0fc7> ACK <of090000030001000000000406> ACK 00090f00030000000000000005 <ACK>

HEON 15 0/1	oven on or off
0F 04 00 03 11 00 19 06
00 04 0F 03 11 00 19 06
GPIB set oven: TMP2 15 45.0 50.0	//45 is SP 50 is max
0F 06 00 03 10 00 01 C2 D9 06 set oven temp
00 04 0F 03 10 00 18 06
0F 06 00 03 12 00 01 F4 ED 06 set max temp
00 04 0F 03 12 00 1A 06

TDIT 15 0 50	autosends info every 5.0 seconds turns autosend on or off
0F 07 00 03 01 01 00 00 32 39 06
00 04 0F 03 01 00 09 06

00 0A 0F 04 01 00 00 00 00 00 01 B6 B7 06	this is the auto temp packet

STOP 15?	doesn’t seem to stop auto temp update

STAT 15	unknown
0F 03 00 02 01 0F 06
00 05 0F 02 01 00 01 08 06

TMPO 15 read current temperature
0F 03 00 02 10 1E 06
00 07 0F 02 10 00 00 01 7C 67 06

ETMP 15 50 sets high point without setting running temp
0F 06 00 03 12 00 00 0A 12 06
00 04 0F 03 12 00 1A 06

00 04 0F 0E 01 02 06 06	volounteered when over temp I think

Init on powerup
00 04 0F 00 01 0F 05 06
0F 04 00 00 01 0F 05 06
02 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF E2 06
02 05 00 30 0D FF 0F CA 06
0D 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF ED 06
0D 05 00 30 0D FF 0F C5 06
0F 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF EF 06
0F 05 00 30 0D FF 0F C7 06
0F 09 00 00 03 00 01 00 00 00 00 04 06
00 09 0F 00 03 00 00 00 00 00 00 05 06

02 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF E2 06
02 05 00 30 0D FF 0F CA 06	//the 0F here might be packet size

Fuzzing:
0005 0F02 1100 0019
Autosampler
Serial address = 0D

get status (OPTC 13) GPIB response = OPTC 13 1 2 -1 0 0
0D 03 00 02 1C 10 06
00 08 0D 02 1C 00 00 00 00 00 1B 06
0D 03 00 02 1B 17 06
00 08 0D 02 1B 00 00 00 00 00 1C 06
0D 03 00 02 14 18 06
00 07 0D 02 14 00 01 02 02 1D 06

STAT 13 STAT 13# 1 1 0
0D 03 00 02 01 0D 06
00 05 0D 02 01 00 00 0B 06
0D 03 00 02 03 0F 06
00 05 0D 02 03 00 01 08 06
0D 03 00 02 04 08 06
00 05 0D 02 04 00 00 0E 06

GPIB wash needle in injection port fast PFM3 13 11 0 0 0
0D 04 00 0A 10 0B 18 06
00 04 0D 0A 10 00 13 06
00 03 0D 08 02 04 06	//started
00 03 0D 08 01 07 06	//volunteers when complete

PFM3 13 12 1 10 5	AS pump wash?
0D 0D 00 0A 10 0C 00 00 01 00 00 0A 00 00 05 18 06
00 04 0D 0A 10 00 13 06
00 03 0D 08 02 04 06
00 03 0D 08 01 07 06

PFM3 13 12 1 10 5 unknown, looks to start and finish something quickly
0D 0D 00 0A 10 0C 00 00 01 00 00 0A 00 00 05 18 06
00 04 0D 0A 10 00 13 06
00 03 0D 08 02 04 06
00 03 0D 08 01 07 06

STMP unknown write
0D 09 00 03 1B 00 00 28 00 00 50 64 06 00 04 0D 03 1B 83 92 06
PTMP unknown write
0D 09 00 03 1C 00 00 28 00 00 50 63 06 00 04 0D 03 1C 83 95 06

OPTC 13
0D 03 00 02 1C 10 06
00 08 0D 02 1C 00 00 00 00 00 1B 06
0D 03 00 02 1B 17 06
00 08 0D 02 1B 00 00 00 00 00 1C 06
0D 03 00 02 14 18 06
00 07 0D 02 14 00 01 02 02 1D 06

APR2 13 GPIB program AS
[4150 5232 2031 33command]20 00[0A wash strokes * 10 (maybe can do partial strokes with a fraction?)] 00[1E injection port wash strokes * 10] 00[02 needle wash speed] 00[04injection port wash speed] 0000 0001 00[02 0002 one of these is syringe volume 1=100, 2=500, 3=1000, 4=2500, 5=5000] 00[04 syringe speed] 00[01 injection method 1 = cut 2=all 3=loop]0000 [0136 cut lead volume] 0000 [0140 cut rear volume] 0000 [014A all feed volume] 0000 [015E loop waste volume] 00[01 needle down speed 1 = slow 2 = fast] (note: it looks like loop injection volume is handled by the injection itself)

4150 5232 2031 3320
000A wash strokes
000A injection port wash strokes
0005 needle wash speed
0005 injection wash speed
0000 0001 unknown
0002 0002 one of these is needle volume
0003 syringe speed
0002 injection method
0000 0136 cut lead volume
0000 0140 cut rear volume
0000 014A all feed volume
0000 015E loop waste volume
00 unknown
01 needle down speed

0D 0C 00 03 13 00 00 0A 00 00 0A 05 05 00 11 06
00 04 0D 03 13 00 19 06
0D 06 00 03 14 01 02 02 1D 06	//the 01 here is likely the rack code 1..16
00 04 0D 03 14 00 1E 06
0D 04 00 03 16 03 1F 06
00 04 0D 03 16 00 1C 06
0D 0F 00 13 15 02 00 01 36 00 01 40 00 01 4A 00 01 3A 06
0D 03 00 30 5E 60 06
00 04 0D 03 15 00 1F 06
0D 04 00 03 17 01 1C 06	//this 01 is likely the pattern 1..16. 1 is row by row 2 is col by col
00 04 0D 03 17 00 1D 06

MNTE 13 is some kind of status maybe? Counts up… seems to be writing to the pump?
02 04 00 07 13 01 13 06
00 0C 02 07 13 00 01 01 00 01 5F 01 1D 03 5B 06

MNTE 13 again <GPIB return> 4D4E 5445 2031 3301 2039 3338 3820 0000 0000 0001 1D03 2039 3338 3820 0000 0000 0001 1D03 2039 3338 3820 0000 0000 0001 1D03 2039 3338 3820 0000 0000 0001 1D03 2020 2020 3020 0000 0000 0000 0000 2020 2020 3020 0000 0000 0000 0000 0D3C

0D 04 00 07 10 01 1F 06
00 0B 0D 07 10 00 01 00 24 AC 01 1D 03 87 06
0D 04 00 07 10 02 1C 06
00 0B 0D 07 10 00 02 00 24 AC 01 1D 03 84 06
0D 04 00 07 10 03 1D 06
00 0B 0D 07 10 00 03 00 24 AC 01 1D 03 85 06
0D 04 00 07 10 04 1A 06
00 0B 0D 07 10 00 04 00 24 AC 01 1D 03 82 06

IJCK 13 possible injection command, call multiple times and eventually is is IJCK 13 0 0
0D 03 00 02 1D 11 06
00 06 0D 02 1D 00 00 00 14 06

SMPL 13 534D 504C 2031 33[20 2020 3532 location] [2020 2020 322E 33 volume][20 2020 2020 31 repeats?]
534D 504C 2031 3320 command
2020 3531 location
2020 2020 312E 32 injection volume?
20 2020 2020 31
0D 0C 00 03 10 00 00 33 00 00 0C 00 00 0A 27 06
00 04 0D 03 10 00 1A 06

Might be volounteered on missing sample:
00 03 0D 01 02 0D

Called just before sample valve switched over
00 04 0D 01 01 02 0B

MODE 13 1? called once. Set to auto maybe? If so, check pump too on same command
0D 04 00 03 03 01 08 06
00 04 0D 03 03 00 09 06

STAT 13
returns STAT 13# 1 1 0
0D 03 00 02 01 0D 06
00 05 0D 02 01 00 00 0B 06
0D 03 00 02 03 0F 06
00 05 0D 02 03 00 01 08 06
0D 03 00 02 04 08 06
00 05 0D 02 04 00 00 0E 06

APR2 13 4150 5232 2031 3320 000A 000A 0005 0005 0000 0001 0002 0002 0003 0002 0000 0136 0000 0140 0000 014A 0000 015E 0001
0D 0C 00 03 13 00 00 0A 00 00 0A 05 05 00 11 06
00 04 0D 03 13 00 19 06
0D 06 00 03 14 01 02 02 1D 06
00 04 0D 03 14 00 1E 06
0D 04 00 03 16 03 1F 06 00 04 0D 03 16 00 1C 06
0D 0F 00 13 15 02 00 01 36 00 01 40 00 01 4A 00 01 3A 06
0D 03 00 30 5E 60 06
00 04 0D 03 15 00 1F 06
0D 04 00 03 17 01 1C 06
00 04 0D 03 17 00 1D 06

Init on power-up
00 04 0D 00 01 0D 05 06
0D 04 00 00 01 0D 05 06
02 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF E2 06
02 05 00 30 0D FF 0F CA 06
0D 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF ED 06
0D 05 00 30 0D FF 0F C5 06
0F 0F 00 10 02 FF 02 FF FF FF FF FF FF FF FF FF FF EF 06
0F 05 00 30 0D FF 0F C7 06
0D 09 00 00 03 00 01 00 00 00 00 06 06
00 09 0D 00 03 00 01 00 00 00 05 03 06
00 03 0D 08 01 07 06
GRCK 13 (get rack paramaters)	4752 434B 2031 3300 [2020 31 pattern or operation pattern]20 [3030 3235 2E30 X1mm] 20[30 3134 372E 30 X2mm]20 [3130 number of vials in X] 20[30 3030 302E 30 Y1mm]20 [3031 3437 2E30 Y2mm] 20[31 32 vials in y]20 [3030 3431 2E30 20 Z height][20 31 pattern or operation pattern]20 [2030 possible operation pattern]

0D 03 00 02 11 1D 06
00 07 0D 02 11 00 00 00 01 18 06
0D 06 00 02 18 00 00 01 10 06
00 0F 0D 12 18 00 00 00 01 00 00 FA 00 05 BE 00 00 48 06
00 0F 0D 20 0A 00 00 00 00 05 BE 00 00 0C 00 01 9A 04 06
00 03 0D 31 01 3E 06

RACK 13 might set the properties

DAD

TIMP 0 0.0 3.0	//sets the start and end time for the DAD in minutes
WTBL 0 0 3	//indicates how many entries exist in table 3, this returns with 68, forces you to call entire table if used
WTBL 0 0 0	498 entries
WTBL 0 0 4	35 entries
WTBL 0 1 3	//starts returning table 3 10 entries at a time with every call
WTBL 0 2 3	//might set table 3 as the active table?
WLRG 0 0 58	sets range of data from range 0 to range 58 from the above table?
TITV 0 32 20	sets spectra update rate to 3200ms, 100ms might be fastest possible
SPCT 0	volounteered at interval
RESP 0 0	called after SPCT is received
ERCL 0	clear errors maybe?
IQEX 0	//check to see if DAD is busy, returns 1 if busy and 0 if not busy
?DAWL 0 45	??? seems like it is related to bandwidth
BNDP 0 2	bandwidth 2=4, 3=8, 1=2 0=1nm, 4=16
SLIT 0 3	set slit to 0=1, 1=2, 2=4, 3=8, 4=16
OLMP 0 1 1	the second 1 is to turn the DAD lamp on. 0 for off
ISLT 0	called before the SLIT command
DAWL 0 22	unknoqn, called after wave table
CZRO 0	unknown
DTYP 0 1 1 1
DTYP 0 1 2 1
DTYP 0 1 3 2
DTYP 0 2 1 2
DTYP 0 2 2 2
TITV 0 16 20

SEND 0 0 1 0
SEND 0 0 3 0
SEND 0 0 3 0
SEND 0 0 2 1
SEND 0 0 1 1	sent before SPCT in calibration
SEND 0 0 3 1
SEND 0 0 1 0
SEND 0 0 2 0

SSPC 0 1	gets spectra?, takes 5 seconds to respond

AZDT 0	Manually get current spectra!
415A 4454 2020 3020 0000 0000 0008 0001 this contains data for the output

SINF 0	get detector info... Scan INFo?
SINF 0 0 3 13 18 4 0 0 Unknown WTBL WLRG start WLRG end BNDP

GLMP 0
GLMP 0 4 0

IERR 0 get current errors
IERR 0 0 0 1 0 0 0 0 0	lamp failure

IDNO	serial number?
IDNO 0 0605030 03 8104853 01

LLOG 0 0 //D2 lamp change date
LLOG 0 1 //Hg lamp change date
BPOS 0 0 //WL adjustment date
LDAT 0 0 04 01 2017 0 0 //set D2 lamp change date
LDAT 0 1 01 01 2000 0 0	//set Hg lamp change date

Calibration:
SEND 0 0 2 0
SEND 0 0 3 0
SEND 0 0 1 0
ISLT 0
BNDP 0 0
WLRG 0 0 497
TITV 0 16 20
TIMP 0 0 50
CALB 0 1 //wait until not busy	possibly turn on Hg lamp?
DMOD 0 1 0 1 1
BPOS 0 0
SEND 0 0 1 0
SLIT 0 0 //wait until not busy
SEND 0 0 1 1
SSPC 0 1
RESP 0 0
SSPC 0 0
RESP 0 0
SEND 0 0 1 0
SLIT 0 1 //wait until not busy
SEND 0 0 1 1
SSPC 0 1
RESP 0 0
SSPC 0 0
RESP 0 0
SEND 0 0 1 0
SLIT 0 2 //wait until not busy
SEND 0 0 1 1
SSPC 0 1
RESP 0 0
SSPC 0 0
SLIT 0 3 //wait
SEND 0 0 1 1
SSPC 0 1
RESP 0 0
SSPC 0 0
RESP 0 0
SEND 0 0 1 0
SLIT 0 4 //wait
SEND 0 0 1 1
SSPC 0 1
RESP 0 0
SSPC 0 0
RESP 0 0
SEND 0 0 1 0
CAED 0 //wait	possibly turn off Hg lamp?
SLIT 0 3 //wait
DMOD 0 0 0 1 1
ZERO 0
BPST 0 1 11 10 10 10 10 06 26 2024	//sets calibration date and calibration
for 2537nm BPST 0 1 10 9 10 10 10 06 26 2024 10 is a WL adjustment of 0. 9 is -1 and 11 is +1
//for 435nm BPST 0 1 11 10 11 10 10 06 26 2024 the 5 numbers relate to the slit
//for 365nm BPST 0 1 11 10 10 10 10 06 26 2024

BPOS 0 x // read the adjustment for slit x=0-4

IQEX responses:
0 = not busy
1 = autozeroing
2 = slit moving
3
4 = CAED calibration
5 = calibration
6
7
8 = DMOD command

Spectra with WLRG = 0, 1	How many tripple 3 bytes are in the message in hex
b'\x00\x00\x00\x00\x02\x00\x01\x00\x00\x00\x00\x00\x00\x00'

Spectra with WLRG = 1, 3
b'\x00\x00\x00\x00\x03\x00\x01\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00'

Spectra with WLRG = 5, 20, BW=2 (not working yet)
b'\x00\x00\x00\x00\x10\x00\x01\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00\x00'

Spectra with WLRG = 10, 11
b'\x00\x00\x00\x00\x02\x00\x01\x00\x00\x00\x00\x00\x00\x00'

None of the following did anything noticible even with either just the address of __0, however, setting the wavetable stopped working a bit for some reason.
SPLS
WLED
FLSB
GSET
WLCK
DAWL
DINP
DOUT
SPRQ
STPS
STRS
SINJ

Auto output
TIMP 0 0.0 600.0
TITV 0 16 20
SEND 0 0 3 0
CZRO 0
GLMP 0
SEND 0 0 2 1
ERCL 0	// clear errors?
STRS 0	// start spectra acquitsition?
SEND 0 0 1 1
SEND 0 0 3 1
//starts sending spectra here

SPRQ 0 1 //stop spectra acquisition?
Detector array physical things:

pin 1 (far inside of unit) = intensity to 10V, resets every 25ms. Seems to start from the side of chip toward the light, each pixel is on/off for 22ms
2 GND
3 -12V
4 GND
5 +12V
6	unknown, was showing 0V
7 GND
8 286 kHz square wave, each pixel is 3 clock pulses with another 3 pulses in the blank period
9 GND
10 5v that pulses to 0V for 14us every every 42us, new pixel starts on falling edge, should be read on rising edge
11 GND
12 5v that pulses to 0V for 21us every every 25ms, the one pixel long pulse indicates the end of what the sensor is able to read. Discard rest of data? Not seeing a start pulse though
13 GND
14 5V supply
15 GND

 IC8 VHC, 244, 9 21
 IC1 PALCE16V8, Z-25SC, 9930DEA
 IC2 same as IC8
 IC5 BB OPA605KP, 0004 7556
 IC6 HA3, 2525-5, H9926BF